# Light Control Service
## Base UUID: 4F770000ED7D-11E4-840E-0002A5D5C51B
## Service UUID: 0x0101
### Abstract:
This service exposes measurement data and control methods for lights intended to use with a bicycle.
### Summary:

### Service Dependencies:
This service is not dependent upon any other service.
### GATT Requirements
Sub-Procedure	Server Requirement
Write Characteristic Value	C1
Notifications	Mandatory
Indications	C1
Read Characteristic Descriptors	Mandatory
Write Characteristic Descriptors	Mandatory

C1: Mandatory if the LC Control Point characteristic is supported, otherwise excluded for this service.
### Transport Dependencies
Transport	Supported
Classic	false
Low Energy	true
High Speed	false

### Error Codes
Name	Code	Description

### Service Characteristics
Overview	Properties	Security	Descriptors
Name: / Light Measurement / Requirement: / Mandatory	Property Requirement / Read Optional / Write Excluded / WriteWithoutResponse Excluded / SigneWrite Excluded / Notify Mandatory / Indicate Excluded / WriteableAuxiliaries Excluded / Broadcast Excluded / ExtendedProperties	None	Overview Permissions / Name: / Client Characteristic Configuration / Requirement: / Mandatory Perm. Req. / Read Mandatory / Write Mandatory
Name: / Light Feature / Requirement: / Mandatory	Property Requirement / Read Mandatory / Write Excluded / WriteWithoutResponse Excluded / SigneWrite Excluded / Notify Excluded / Indicate Excluded / WriteableAuxiliaries Excluded / Broadcast Excluded / ExtendedProperties	None	None
Name: / Light Control Point / Requirement: / Optional	Property Requirement / Read Excluded / Write Mandatory / WriteWithoutResponse Excluded / SigneWrite Excluded / Notify Excluded / Indicate Mandatory / WriteableAuxiliaries Excluded / Broadcast Excluded / ExtendedProperties	None	Overview Permissions / Name: / Client Characteristic Configuration / Requirement: / Mandatory Perm. Req. / Read Mandatory / Write Mandatory

# Light Measurement
## Characteristic UUID: 0x0102
### Summary:
The Light Measurement characteristic is a variable length structure containing a Flags field and, based on the contents of the Flags field, may contain one or more additional fields as shown in the table below.
### Value Fields
Names	Field Req.	Format	Additional Information
Flags	Mandatory	16bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Intensity Field Present 0 True / 1 False / 1 1 Flood Status Field Present 0 True / 1 False / 2 1 Spot Status Field Present 0 True / 1 False / 3 1 Flood Output Power Field Present 0 True / 1 False / 4 1 Spot Output Power Field Present 0 True / 1 False / 5 1 Temperature Field Present 0 True / 1 False / 6 1 Input Voltage Field Present 0 True / 1 False / 7 1 Pitch Field Present 0 True / 1 False / 8 8 Reserved fur future use
Mode	Mandatory	uint8	Enumerations: / Key Value / 0 Off / 1 Flood / 2 Spot / 3 Flood & Spot / 4 Flood Pitch Compensated / 5 Spot & Pitch Compensated / 6 Flood & Spot Pitch Compensated / 7 Flood (both driver used) / 8 Spot (both drivers used) / 9 Flood Pitch Compensated (both drivers used) / 10 Spot Pitch Compensated (both drivers used) / 11-255 Reserved for future use
Intensity / Information: / Unit is is in percentage with a resolution of 1, in relation to maximum output power. / In an adaptive mode unit is in lux with a resolution of 1, representing the illuminance under intended use / Unit: / org.bluetooth.unit.percentage / org.bluetooth.unit.illuminance.lux / Exponent: Decimal, 0	Optional	uint8	None
Flood Status	Optional	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Overcurrent Indicator 0 Not active / 1 active / 1 1 Voltage Limiting Indicator 0 Not active / 1 active / 2 1 Temperature Limiting Indicator 0 Not active / 1 active / 3 1 Duty Cycle Limit Indicatior 0 Not active / 1 active / 4 4 Reserved fur future use
Spot Status	Optional	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Overcurrent Indicator 0 Not active / 1 active / 1 1 Voltage Limiting Indicator 0 Not active / 1 active / 2 1 Temperature Limiting Indicator 0 Not active / 1 active / 3 1 Duty Cycle Limit Indicatior 0 Not active / 1 active / 4 4 Reserved fur future use
Flood Output Power / Information: / Unit is in watts with a resolution of 1/1000. / Unit: / org.bluetooth.unit.power.watt / Exponent: Decimal, -3	Optional	uint16
Spot Output Power / Information: / Unit is in watts with a resolution of 1/1000. / Unit: / org.bluetooth.unit.power.watt / Exponent: Decimal, -3	Optional	uint16
Temperature / Information: / Unit is in degree Celsius with a resolution of 1. / Unit: / org.bluetooth.unit.thermodynamic_temperature.degree_celsius / Exponent: Decimal, 0	Optional	int8
Input Voltagge / Information: / Unit is in volts with a resolution of 1/1000. / Unit: / org.bluetooth.unit.electric_potential_difference.volt / Exponent: Decimal, -3	Optional	uint16
Pitch / Information: / Unit is in degree with a resolution of 1. / Unit: / org.bluetooth.unit.plane_angle.degree / Exponent: Decimal, 0	Optional	int8

# Light Feature
## Characteristic UUID: 0x0103
### Summary:
The Light Feature characteristic is used to report a list of features supported by the device.
### Value Fields
Names	Field Req.	Format	Additional Information
Light Feature	Mandatory	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Flood Supported 0 True / 1 False / 1 1 Spot Supported 0 True / 1 False / 2 1 Pitch Compensation Supported 0 True / 1 False / 3 1 Mode Change Supported 0 True / 1 False / 4 1 Mode Configuration Supported 0 True / 1 False / 5 1 Mode Grouping Supported 0 True / 1 False / 6 1 LED configuration check supported 0 True / 1 False / 7 1 Reserved fur future use 1

# Light Control Point
## Characteristic UUID: 0x0104
### Summary:
The Light Control Point characteristic is used to request a specific function to be executed on the receiving device.
### Value Fields
Names	Field Req.	Format	Additional Information
Op Codes	Mandatory	uint8	Enumerations / Key Value Description / 1 Request mode Count Request the number of modes supported by the light. The response is Op Code 0x20 followed by the mode count (in uint8). The maximum number of supported modes is 16 and has always to be a power of 2. / 2 Request group configuration Request current mode grouping configuration. The response is Op Code 0x20 followed by the current number of groups (in uint8). The number of modes available in each group is the quotient of mode count and group count. / 3 Request mode configuration Request a list of mode configurations. The mode list start number is sent as uint8 with preceding Op Code 0x03 operand. The response to this control point is Op Code 0x20 followed by the list as response parameter. / NOTE: If the list exceeds the maximum length of the indication packet it will be truncated. To receive the complete list of modes the host has to call this procedure multiple times wirh different start values. / 4 Set Mode Initiate the procedure to put the light into a specific mode. The requested mode is sent as an uint8 with preceding Op Code 0x04 operand. The response to this control point is Op Code 0x20. / To put the light in off mode send an invalid mode number. / 5 Configure Mode Initiate the procedure to change a set of mode configurations. The new configurations are sent as an uint8 (representing the first mode number to change) followed by a list of configurations (each containing an uint8 representing the mode and an uint8 representing the intensity) with preceding Op Code 0x05 operand. The response to this control point is Op Code 0x20 / 6 Configure Group Initiate the procedure to change the group configuration. The new number of groups (must be a power of two) is sent as an uint8 with preceding Op Code 0x06 operand. The response to this control point is Op Code 0x20. / 7 Request LED configuration Request the LED configuration setup. The response is Op Code 0x20 followed by the number of installed LEDs of the flood driver followed by the number if LEDS if the spot driver. / 8 Strat LED configuration check Initiate the procedure to start the detection of installed LED configuration. The response to this control point is Op Code 0x20 followed by the number of installed LEDs of the flood driver followed by the number if LEDS if the spot driver. / 32 Response Code The response code is followed by the requested Op Code, the response value and optionaly the response parameter / 0-0 Reserved for future use / 9-31 Reserved for future use / 33-255 Reserved for future use
Parameter Value	Optional	variable	Refer to the Op Code table above for additional information on the possible values for this filed
Request Op Code / Information: / The Request Op Code is a sub field of the Parameter Value for "Response Code" Op Code. C1: This Field is Mandatory for "Response Code" Op Code, otherwise this field is Excluded.	C1	uint8	Refer to the Op Code table above for additional information on the possible values for this filed
Response Value / Information: / The Request Op Code is a sub field of the Parameter Value for "Response Code" Op Code. C1: This Field is Mandatory for "Response Code" Op Code, otherwise this field is Excluded.	C1	uint8	Enumerations / Key Value Description / 1 Success Response for successful operation. / 2 Op Code not supported Response if unsupported Op Code is received. / 3 Invalid Parameter Response if Parameter received does not meet the requirements of the service or is outside of the supported range of the Light. / 4 Operation Failed Response if the requested procedure failed / 0-0 Reserved for future use / 5-255 Reserved for future use
Response Parameter / Information: / The Response Parameter is a sub field of the Parameter Value for "Response Code" Op Code. C2:This Field is Optional for "Response Code" Op Code, otherwise this field is Excluded.	C2	variable	Note: The Response Parameter Value of the response to the Control Point is a variable length field to allow a list of different values defined by the Service Specification