# Light Control Service
## Base UUID: 4F770000ED7D-11E4-840E-0002A5D5C51B
## Service UUID: 0x0101
### Abstract:
This service exposes measurement data and control methods for lights intended to use with a bicycle.
### Summary:

### Service Dependencies:
This service is not dependent upon any other service.
### GATT Requirements
Sub-Procedure	Server Requirement
Write Characteristic Value	C1
Notifications	Mandatory
Indications	C1
Read Characteristic Descriptors	Mandatory
Write Characteristic Descriptors	Mandatory

C1: Mandatory if the LC Control Point characteristic is supported, otherwise excluded for this service.
### Transport Dependencies
Transport	Supported
Classic	false
Low Energy	true
High Speed	false

### Error Codes
Name	Code	Description

### Service Characteristics
Overview	Properties	Security	Descriptors
Name: / Light Measurement / Requirement: / Mandatory	Property Requirement / Read Optional / Write Excluded / WriteWithoutResponse Excluded / SignedWrite Excluded / Notify Mandatory / Indicate Excluded / WriteableAuxiliaries Excluded / Broadcast Excluded / ExtendedProperties	None	Overview Permissions / Name: / Client Characteristic Configuration / Requirement: / Mandatory Perm. Req. / Read Mandatory / Write Mandatory
Name: / Light Feature / Requirement: / Mandatory	Property Requirement / Read Mandatory / Write Excluded / WriteWithoutResponse Excluded / SignedWrite Excluded / Notify Excluded / Indicate Excluded / WriteableAuxiliaries Excluded / Broadcast Excluded / ExtendedProperties	None	None
Name: / Light Control Point / Requirement: / Optional	Property Requirement / Read Excluded / Write Mandatory / WriteWithoutResponse Excluded / SignedWrite Excluded / Notify Excluded / Indicate Mandatory / WriteableAuxiliaries Excluded / Broadcast Excluded / ExtendedProperties	None	Overview Permissions / Name: / Client Characteristic Configuration / Requirement: / Mandatory Perm. Req. / Read Mandatory / Write Mandatory

# Light Measurement
## Characteristic UUID: 0x0102
### Summary:
The Light Measurement characteristic is a variable length structure containing a Flags field and, based on the contents of the Flags field, may contain one or more additional fields as shown in the table below.
### Value Fields
Names	Field Req.	Format	Additional Information
Light Type	Mandatory	8bit	Enumeration / Key Value / 0 Helmet Light / 1 Bike Light / 2 Tail Light / 3-255 Reserved for future use
Flags	Mandatory	16bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Intensity(s) Field Present 0 False / 1 True / 1 1 Flood/Main Beam Status Field Present 0 False / 1 True / 2 1 Spot/High Beam Status Field Present 0 False / 1 True / 3 1 Flood/Main Beam Output Power Field Present 0 False / 1 True / 4 1 Spot/High Beam Output Power Field Present 0 False / 1 True / 5 1 Temperature Field Present 0 False / 1 True / 6 1 Input Voltage Field Present 0 False / 1 True / 7 1 Pitch/Inclination Field Present 0 False / 1 True / 8 1 Battery SOC Present 0 False / 1 True / 9 7 Reserved fur future use
Helmet Setup	Mandatory for Light Type “Helmet Light”, otherwise excluded	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Flood active 0 False / 1 True / 1 1 Spot active 0 False / 1 True / 2 1 Pitch compensation 0 Disabled / 1 Enabled / 3 1 Output cloned 0 False / 1 True / 4 1 External Taillight 0 Disabled / 1 Enabled / 5 1 External Brake-light 0 Disabled / 1 Enabled / 6 2 Reserved fur future use
Bike Setup	Mandatory for Light Type “Bike Light”, otherwise excluded	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Main Beam active 0 False / 1 True / 1 1 Extended Main Beam active 0 False / 1 True / 2 1 High Beam active 0 False / 1 True / 3 1 Daylight active 0 Disabled / 1 Enabled / 4 1 External Taillight 0 Disabled / 1 Enabled / 5 1 External Brake-light 0 Disabled / 1 Enabled / 6 2 Reserved fur future use
Taillight Setup	Mandatory for Light Type “Taillight”, otherwise excluded
Helmet Intensity / Information: / Unit is is in percentage with a resolution of 1, in relation to maximum output power. / In a setup with activated pitch compensation the unit is in lux with a resolution of 1, representing the luminescence under intended use / Unit: / org.bluetooth.unit.percentage / org.bluetooth.unit.illuminance.lux / Exponent: Decimal, 0	Optional for Light Type “Helmet Light”, otherwise excluded	uint8
Main Beam Intensity / Information: / Unit is is in percentage with a resolution of 1, in relation to maximum output power. / Unit: / org.bluetooth.unit.percentage / Exponent: Decimal, 0	Optional for Light Type “Bike Light”, otherwise excluded	uint8
High Beam Intensity / Information: / Unit is is in percentage with a resolution of 1, in relation to maximum output power. / Unit: / org.bluetooth.unit.percentage / Exponent: Decimal, 0	Optional for Light Type “Bike Light”, otherwise excluded	uint8
Flood Status	Optional for Light Type “Helmet Light”, otherwise excluded	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Over-current Indicator 0 Not active / 1 active / 1 1 Voltage Limiting Indicator 0 Not active / 1 active / 2 1 Temperature Limiting Indicator 0 Not active / 1 active / 3 1 Duty Cycle Limit Indicator 0 Not active / 1 active / 4 4 Reserved fur future use
Main Beam Status	Optional for Light Type “Bike Light”, otherwise excluded	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Over-current Indicator 0 Not active / 1 active / 1 1 Voltage Limiting Indicator 0 Not active / 1 active / 2 1 Temperature Limiting Indicator 0 Not active / 1 active / 3 1 Duty Cycle Limit Indicator 0 Not active / 1 active / 4 4 Reserved fur future use
Spot Status	Optional for Light Type “Helmet Light”, otherwise excluded	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Over-current Indicator 0 Not active / 1 active / 1 1 Voltage Limiting Indicator 0 Not active / 1 active / 2 1 Temperature Limiting Indicator 0 Not active / 1 active / 3 1 Duty Cycle Limit Indicator 0 Not active / 1 active / 4 4 Reserved fur future use
High Beam Status	Optional for Light Type “Bike Light”, otherwise excluded	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Over-current Indicator 0 Not active / 1 active / 1 1 Voltage Limiting Indicator 0 Not active / 1 active / 2 1 Temperature Limiting Indicator 0 Not active / 1 active / 3 1 Duty Cycle Limit Indicator 0 Not active / 1 active / 4 4 Reserved fur future use
Flood Output Power / Information: / Unit is in watts with a resolution of 1/1000. / Unit: / org.bluetooth.unit.power.watt / Exponent: Decimal, -3	Optional for Light Type “Helmet Light”, otherwise excluded	uint16
Main Beam Output Power / Information: / Unit is in watts with a resolution of 1/1000. / Unit: / org.bluetooth.unit.power.watt / Exponent: Decimal, -3	Optional for Light Type “Bike Light”, otherwise excluded	uint16
Spot Output Power / Information: / Unit is in watts with a resolution of 1/1000. / Unit: / org.bluetooth.unit.power.watt / Exponent: Decimal, -3	Optional for Light Type “Helmet Light”, otherwise excluded	uint16
High Beam Output Power / Information: / Unit is in watts with a resolution of 1/1000. / Unit: / org.bluetooth.unit.power.watt / Exponent: Decimal, -3	Optional for Light Type “Bike Light”, otherwise excluded	uint16
Temperature / Information: / Unit is in degree Celsius with a resolution of 1. / Unit: / org.bluetooth.unit.thermodynamic_temperature.degree_celsius / Exponent: Decimal, 0	Optional	int8
Input Voltage / Information: / Unit is in volts with a resolution of 1/1000. / Unit: / org.bluetooth.unit.electric_potential_difference.volt / Exponent: Decimal, -3	Optional	uint16
Pitch / Information: / Unit is in degree with a resolution of 1. / Unit: / org.bluetooth.unit.plane_angle.degree / Exponent: Decimal, 0	Optional for Light Type “Helmet Light”, otherwise excluded	int8
Inclination / Information: / Unit is in degree with a resolution of 1. / Unit: / org.bluetooth.unit.plane_angle.degree / Exponent: Decimal, 0	Optional for Light Type “Bike Light”, otherwise excluded	int8
Battery State of Charge / Information: / Unit is is in percentage with a resolution of 1 / Unit: / org.bluetooth.unit.percentage / Exponent: Decimal, 0	Optional	uint8

# Light Feature
## Characteristic UUID: 0x0103
### Summary:
The Light Feature characteristic is used to report a list of features supported by the device.
### Value Fields
Names	Field Req.	Format	Additional Information
Light Type	Mandatory	8bit	Enumeration / Key Value / 0 Helmet Light / 1 Bike Light / 2 Tail Light / 3-255 Reserved for future use
Configuration Features	Mandatory	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Mode Change Supported 0 False / 1 True / 1 1 Mode Configuration Supported 0 False / 1 True / 2 1 Mode Grouping Supported 0 False / 1 True / 3 1 Preferred Mode Supported 0 False / 1 True / 4 1 Temporary Mode Supported 0 False / 1 True / 5 3 Reserved for future use
Setup Features	Mandatory	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 LED configuration check supported 0 False / 1 True / 1 1 Sensor offset calibration supported 0 False / 1 True / 2 1 Current limitation supported 0 False / 1 True / 3 5 Reserved for future use
Helmet Light Feature	Mandatory for devices of type Helmet Light, otherwise excluded	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Flood Supported 0 False / 1 True / 1 1 Spot Supported 0 False / 1 True / 2 1 Pitch Compensation Supported 0 False / 1 True / 3 1 Driver Cloning Supported 0 False / 1 True / 4 1 External Taillight supported 0 False / 1 True / 5 1 External Brake-light supported 0 False / 1 True / 6 2 Reserved fur future use 1
Bike Light Feature	Mandatory for devices of type Bike Light, otherwise excluded	8bit	Bit Field / Bit Size Name Definition / Key Value / 0 1 Main Beam Supported 0 False / 1 True / 1 1 Extended Main Beam Supported 0 False / 1 True / 2 1 High Beam Supported 0 False / 1 True / 3 1 Daylight Supported 0 False / 1 True / 4 1 External Taillight supported 0 False / 1 True / 5 1 External Brake-light supported 0 False / 1 True / 6 2 Reserved fur future use
Tail Light Feature	Mandatory for devices of type Tail Light, otherwise excluded	16bit	tbd.

# Light Control Point
## Characteristic UUID: 0x0104
### Summary:
The Light Control Point characteristic is used to request a specific function to be executed on the receiving device.
### Value Fields
Names	Field Req.	Format	Additional Information
Op Codes	Mandatory	uint8	Enumerations / Key Value Description / 1 Request mode Count Request the number of modes supported by the light. The response is Op Code 0x20 followed by the mode count (in uint8). The maximum number of supported modes is 16 and has always to be a power of 2. / 2 Set Mode Initiate the procedure to put the light into a specific mode. The requested mode is sent as an uint8 with preceding Op Code 0x02 operand. The response to this control point is Op Code 0x20. / To put the light in off mode send an invalid mode number. / 3 Request group configuration Request current mode grouping configuration. The response is Op Code 0x20 followed by the current number of groups (in uint8). The number of modes available in each group is the quotient of mode count and group count. / 4 Set group configuration Initiate the procedure to change the group configuration. The new number of groups (must be a power of two) is sent as an uint8 with preceding Op Code 0x04 operand. The response to this control point is Op Code 0x20. / 5 Request mode configuration Request a list of mode configurations. The mode list start number is sent as uint8 with preceding Op Code 0x05 operand. The response to this control point is Op Code 0x20 followed by the list as response parameter. / NOTE: If the list exceeds the maximum length of the indication packet it will be truncated. To receive the complete list of modes the host has to call this procedure multiple times with different start values. / 6 Set mode configuration Initiate the procedure to change a set of mode configurations. The new configurations are sent as an uint8 (representing the first mode number to change) followed by a list of configurations (each containing an uint8 representing the setup and an uint8 representing the intensity, respectively two uint8 for main and high beam) with preceding Op Code 0x06 operand. The response to this control point is Op Code 0x20 / 7 Request LED configuration Request the LED configuration setup. The response is Op Code 0x20 followed by the number of installed LEDs of the flood/main beam driver followed by the number if LEDs if the spot/high beam driver. / 8 Start LED configuration check Initiate the procedure to start the detection of installed LED configuration. The response to this control point is Op Code 0x20 followed by the number of installed LEDs of the flood/main beam driver followed by the number if LEDs if the spot/high beam driver. / 9 Request Sensor Offset Request the current Sensor Offset Values. The response is Op Code 0x20 followed by the offset values for x, y, z axis (in int16 each). If no offset values are available yet, the response value shall be set to 0x04. / 10 Start Sensor Offset Calibration Initiate the procedure to start the sensor offset calibration. The response to this control point is 0x20 followed by the new offset values for x, y and z-axis (int16 each). / 11 Request Current Limit Request the current current limits. The response is Op Code 0x20 followed by the current limits (in int8 representing %) / 12 Set Current Limit Initiate the procedure to change the current limits. The new limits is sent as a pair of int8 (the first representing the limit for flood/main beam, the second for spot/high beam, both in %) with preceding Op Code 0x0C operand. The response to this control point is Op Code 0x20. / 13 Request Preferred Mode Request the currently preferred mode. The response is Op Code 0x20 followed by the preferred mode. If no preferred mode is set, the response is an invalid mode number / 14 Set Preferred Mode Initiate the procedure to set the preferred mode. The new preferred mode is sent as an uint8 with preceding Op Code 0x02 operand. The response to this control point is Op Code 0x20. / To disable the preferred mode send an invalid mode number. / 15 Request Temporary Mode Request the current temporary mode. The response is Op Code 0x20 followed by the preferred mode. If no temporary mode is set, the response is an invalid mode number / 16 Set Temporary Mode Initiate the procedure to set the temporary mode. The new temporary mode is sent as an uint8 with preceding Op Code 0x02 operand. The response to this control point is Op Code 0x20. / To disable the temporary mode send an invalid mode number. / 32 Response Code The response code is followed by the requested Op Code, the response value and optionally the response parameter / 0-0 Reserved for future use / 17-31 Reserved for future use / 33-255 Reserved for future use
Parameter Value	Optional	variable	Refer to the Op Code table above for additional information on the possible values for this filed
Request Op Code / Information: / The Request Op Code is a sub field of the Parameter Value for "Response Code" Op Code. C1: This Field is Mandatory for "Response Code" Op Code, otherwise this field is Excluded.	C1	uint8	Refer to the Op Code table above for additional information on the possible values for this filed
Response Value / Information: / The Request Op Code is a sub field of the Parameter Value for "Response Code" Op Code. C1: This Field is Mandatory for "Response Code" Op Code, otherwise this field is Excluded.	C1	uint8	Enumerations / Key Value Description / 1 Success Response for successful operation. / 2 Op Code not supported Response if unsupported Op Code is received. / 3 Invalid Parameter Response if Parameter received does not meet the requirements of the service or is outside of the supported range of the Light. / 4 Operation Failed Response if the requested procedure failed / 0-0 Reserved for future use / 5-255 Reserved for future use
Response Parameter / Information: / The Response Parameter is a sub field of the Parameter Value for "Response Code" Op Code. C2:This Field is Optional for "Response Code" Op Code, otherwise this field is Excluded.	C2	variable	Note: The Response Parameter Value of the response to the Control Point is a variable length field to allow a list of different values defined by the Service Specification